## Slide 1: MQTT Laboratory - ABB IRB1600
Digital Twin, IoT Communication, and Robotics Integration
Balog Bogdan Gheorghe

## Slide 2: Overview
In this laboratory, you will explore MQTT communication for robotics.
The goal is to understand how to connect Python, ESP8266, and industrial robots using MQTT as a communication protocol for IoT systems.

## Slide 3: What Is MQTT?
MQTT (Message Queuing Telemetry Transport) is a lightweight, low-bandwidth protocol for machine-to-machine (M2M) communication.
It is commonly used in IoT applications where devices need to exchange small data packets efficiently.
Source: https://www.spiceworks.com/tech/iot/articles/what-is-mqtt/

## Slide 4: Task 1 - Python & Robot IRB1600
This task demonstrates how Python can control a robot (IRB1600) through MQTT messages.
A Python MQTT client listens for messages from a broker and forwards commands via a TCP socket to the robot.
Video Reference: https://youtu.be/E-Gvn6QCAYc

## Slide 5: Task 1 - Code Summary
The Python script performs the following steps:
1. Connects to an MQTT broker and subscribes to 'button_topic/mqtt'.
2. Listens for messages.
3. Opens a TCP connection to the robot (192.168.125.1:1500).
4. Sends control commands ('aplicatia_1' or 'aplicatia_2').
5. Receives and prints the robot's response.

## Slide 6: Publisher MQTT Interface
A Python GUI using Tkinter publishes MQTT messages via button presses.
Features:
- Three buttons with images.
- Each button sends a message to the MQTT topic when clicked.
- Displays connection status ('Connected' / 'Not Connected').
- Uses Paho MQTT library for communication.

## Slide 7: Task 2 - ESP8266 Subscriber
This task demonstrates MQTT communication between a phone app and an ESP8266 microcontroller.
The ESP8266 subscribes to 'xarm/variables' and blinks its onboard LED based on JSON messages received via MQTT.
Example JSON:
{ 'variable1': 'a', 'variable2': 5 } → LED blinks 5 times at 1-second intervals.

## Slide 8: ESP8266 Workflow
1. Connects to Wi-Fi and MQTT broker.
2. Subscribes to topic 'xarm/variables'.
3. Parses JSON messages with ArduinoJson.
4. Queues commands for sequential processing.
5. Controls LED blinking based on received instructions.

## Slide 9: Summary
• Python and ESP8266 both use MQTT for robot and IoT communication.
• MQTT ensures low-latency and efficient data exchange.
• Digital Twin mirrors real-time robot actions.
• This lab integrates Robot + Python + ESP8266 over MQTT.